## Slide 1: Round beams at Petra IV
Ilya Agapov
NOCO2017, Arcidosso, 19-22 September 2017

## Slide 2: Contents
Petra IV – the Petra III upgrade project
Round beams on coupling resonance – experience at Petra III
Twist lattice
Nonlinear dynamics aspects in the twist lattice

## Slide 3: Petra IV
2.3 km circumference 1.6 km bending radius
10-30 pm emittance range from scaling of various MBA lattices possible
~10 pm diffraction limit at 10 keV in 2015 (20 keV in 2017)
From Liu Lin IPAC 2017

## Slide 4: Petra IV
PETRA III DBA + FODO
Want to upgrade to MBA

## Slide 5: PETRA IV project study: time schedule

## Slide 6: Petra IV challenges
Opportunities are challenges at the same time
Campus: existing infrastructure but not much freedom to build new exp halls; semi-underground tunnel
Long straights – long IDs, beam manipulation
Usual DLSR challenges
  Nonlinear dynamics
  Vacuum
  Magnet design
  Vibrations, stability, alignment
PETRA IV Parameter | 
Energy | 6 GeV (4.5 – 6 GeV)
Current | 100 mA (100 – 200 mA)
Number of bunches | ~ 1000
Emittance horz. | 10 pm rad (10 – 30 pm rad)
vert. | 10 pm rad (10 – 30 pm rad)
Bunch length | ~ 100 ps

## Slide 7: Petra IV lattice based on ESRF design
Different scaling/modifications applied to the ESRF-EBS cell
Scaling : if 1/f and g are the angle and length scaling factors, with appropriate magnet strength scaling same optics, emittance scales as 1/f3,DA as g/f2
  Option 1: 23m length., 5o. (9 cells arc, same ID pos.), ~10pm
  Option 2: ~29m length., 6.3o. (7 cells arc), ~24 pm
  Option 3: ~ 25 m, 5.6o. (8 cells arc) ~14 pm
Similar design, but with 6 bends (H6BA), can also give 24 pm
H7BA
H6BA

## Slide 8: PETRA IV-Ring with H7BA 25.2 m cells and DW
Parameter | Value
Energy E | 6 GeV
Length L | 2304 m
Tune Qx/Qy | 163.17 / 67.27
Nat. chromaticity ξx/ξy | -228.8 / -190.9
Damping part. number Jx | 1.145
Nat. emittance x | 9.3 pm*rad
MCF αc | 0.015e-3
Energy spread e | 1.425e-3
Hor. damping time x | 17.3 ms
Ver. damping time y | 19.8 ms
Long. damping time e | 10.7 ms
Energy loss per turn U0 | 4.6 MeV
βx at ID | 6.6 m
βy at ID | 2.1 m
Dx at ID | 0 m
Free space L at ID | 5.0 m
Zero-current values – without IBS!
Long straight section in W: damping wigglers
Parameters: 10 DW, LDW=4 m, BDW=1.5 T, λDW=4.5 cm
Hor. beta peak of 100 m (“Injection”) in S
Phase advance in long (short) straights: planes Δφx,y= 1(2) + qx,y/8
Damping
Wigglers
Injection
βx=100 m

## Slide 9: Brilliance Comparision
PETRA III
  εx = 1.2 nm,
  κ = 0.25%
PETRA IV
  εx,y = 15 pm round
  βx=5m, βy=2.5m
   increase by 100x at 80keV
PETRA IV aggressive design
  εx = 10 pm
  κ = 50%
  βx,y = 1m
all calculations for 6GeV
UE65
U29_5m
CPMU_4m
U32_4*5m
IVU21_4m

## Slide 10: Coherent Flux Comparision
PETRA III
  εx = 1.2 nm,
  κ = 0.25%
PETRA IV
  εx,y = 15 pm round
  βx=5m, βy=2.5m
   increase by ~40x at 80keV
PETRA IV aggressive design
  εx = 10 pm
  κ = 50%
  βx,y = 1m
   increase by ~200x at 80keV

## Slide 11: Effect of energy spread
Energy spread to be minimized – try to avoid damping wigglers
beta_x,y = 1m (solid), 2m (dashed), 5m (dotted)

## Slide 12: Touschek Lifetime
Simplified analytical model with averaged optical functions
For very small emittances Touschek lifetime will rise again
A larger momentum acceptance shifts the lifetime minimum to higher emittances
From Piwinski’s formula: For  > 5 h in the range of 10-30 pm·rad a momentum acceptance of > 2% is needed
  Conditions: E = 6 GeV, round beam, N = 1010 particles in bunch <bx> = 4.8 m, <by> = 8.9 m, <Dx> = 1.3 cm , σs=1 cm, σp = 10-3 (scaled ESRF-H7BA-cell)
10 pm
20 pm
2.5%
2%
1.5%

## Slide 13: IBS and Touschek Lifetime (500 MHz, 10% coupling)
Energy spread is wiggler dominated!
3 mm → 13 ps
Energy spread ≈1.5·10-3
Wiggler dominated
εx
εy
80 bunches
960 bunches

## Slide 14: IBS and Touschek Lifetime (100 MHz, 100% coupling)
Energy spread is wiggler dominated!
7 mm → 23 ps
Energy spread ≈1.5·10-3
Wiggler dominated
ε x=εy
80 bunches
768 bunches

## Slide 15: Petra IV reference lattice open issues
DA ~ 1 mm mrad w/o errors – 1cm at injection point. Trying to improve
Alignment tolerances very tight (few mu m rms)
Magnet strengths to be reduced (sextupole)
MOGA extremely cpu and time-consuming

## Slide 16: Round beams
Some applications could benefit from round beams
Smaller IBS growth rates
But:
Brightness counts
Beamline optics counts
P09
Matsushita http://cheiron2010.spring8.or.jp/
benchmark optics

## Slide 17: Round beams -- methods
Wigglers
Coupling
  Resonance
  Moebius and modifications (Novosibirsk, Cornell, PSI,…)

## Slide 18: Petra III
Bringing tunes to coupling resonance routinely for coupling correction
IBS measurements at 3 GeV in 2013
Recent campaign – try to achieve operational parameters with round beam
3 GeV measurement
Jan 2013

## Slide 19: Petra III details on coupling resonance
Emittance ratio Guignard Phys. Rev, E 51, 6 1995
g =
20.45 kHz (Qx=Qy=0.157)
24.6 kHz (Qx=Qy=0.19)
Separation 2kHz = 0.01

## Slide 20: Petra III details on coupling resonance
BB measurement with LOCO – 10% BB at source
Unfortunately works only on a neighbouring tune
Operational considerations on resonance
Need to correct and measure optics (dispersion, BB) – more difficult on resonance
If coupling is well corrected – resonance narrow, intensity drop moves tune away
Resonance broad – getting vertical dispersion; Balance to be understood
Need to figure out optimal injection scheme (e.g. inject close to resonance, broaden with skew)

## Slide 21: Petra III details on coupling resonance
Results
Getting round beam within 10-20% measurement uncertainty
Approx. half emittance (down to 800/700; flat beam ~1500/15 ) only close to the original WP. At tunes around 0.24 getting vertical emittance blowup without reduction in hor.
Store 2.7 mA per single bunch (same as present high charge mode)
TODO: optimize working point, try to store 100 mA
Top-up probably impossible
2D interferometric system:
A. Novokshonov et al., proc IPAC 2017
A. Novokshonov et al., proc IBIC 2016

## Slide 22: Other lattices for Petra IV – exploiting geometry
Hybrid 7BA lattice used for CDR studies
However with 6/8 arcs having no IDs this is not optimal
Looking into alternative lattices

## Slide 23: Twist lattice
A lattice based on following concepts
Non-interleaved sextupole scheme
Non-local chromaticity correction
Phase space exchange (Twist)

## Slide 24
Phase space exchange optics (TMBA)
x,y = 
SF
SF
3 arc octants
injection section
undulator sections
x = hor., y = vert.
3 arc octants
y=hor., x=vert.
y/x
x/y
part 1
part 2
Phase space exchange (twist)
Concept to significantly improve DA (suggested for Petra R. Brinkmann Ideenmarkt 2015)
Two phase space exchanges in the ring (similarity to Möbius scheme, but optics is always in one mode locally)
Only sum chromaticity is corrected, allows to have a –I sextupole arrangement

## Slide 25: TMBA cells
Cells for arcs with and w/o IDs, 1 sextupole family, with π/π phase advance (-I transform)
Can be used in combination with non-local chromaticity correction (2 cells, arc, ring etc.)
H7BA cell with one sextupole family can be used in the same way
Cell layout, emittance range 35-50 pm
Cell with no ID space based on same principle, emittance range 25-30 pm
Extra large on-momentum acceptance

## Slide 26: TMBA optics
Version 0 -I 6BA no-ID arc cells, versions 1 and 2: -I 6BA no-ID arc and undulator cells
2-fold symmetry broken by injection region – superperiod 1
v1-v3 with two cell types
v0 (blue): only no-ID cell, 2 twists, 8 straights tracking with RF
v2 (green): added undulator cell and injection point
25/25 pm lattice

## Slide 27: TMBA optics features
On-momentum DA no problem. Limitation– path lengthening excites synchrotron oscillations – limited by longitudinal acceptance
2nd and higher order chromaticity limiting MA – not very different from the reference lattice
Optics has larger DA and smaller MA than HMBA. Work in progress to improve MA
Off-axis injection still non-trivial, but at least the oscillations are controllable and can be adjusted to the aperture
Ideally one would want to have the twist optics as and advanced option

## Slide 28: Simplified model with two arcs (no twist)
q1 q2 dq1 dq2
0.1702368928 0.2135912064 0.7212729468 0.8111877208
Test, 10xcell B per arc
Footprint for momentum deviation, MA +-5 % (x0=y0=1 mu m)
Tracking vs analytical(ptc) up to 5th order

## Slide 29: Toy model nonlinear dynamics gallery
Model: Matrix x Twist x Sextupole1 x Matrix x Twist x Sextupole2
0-aplitude tune close to 1/3 resonance

## Slide 30: Toy model nonlinear dynamics gallery
Large amplitude stability destroyed by phase detuning order 10^-2
Close to ¼ resonance – trajectories irregular for much smaller amplitudes

## Slide 31: Toy model : Phase space with and w/o twist
Close to ¼
On and close to 1/3

## Slide 32: Toy model
No twist stability diagram x=y=0.5
Qy/2
Qx/2
With twist stability diagram x=y=0.5 Similar pattern for other initial conditions

## Slide 33: Toy model nonlinear dynamics gallery
DA example, 0.1/0.1 phase advances
DA example, 0.32/0.32 phase advances
twist

## Slide 34: Conclusion
Petra IV lattice design is underway, with 10 pm H7BA 25m cell optics as current reference
Round beams could be and important option
Working on the coupling resonance is possible
Twist lattice investigated.
Simplified model of the twist lattice suggests that the dynamics with a twist can be more sensitive to the phase advance selection
However the twist allows for –I sextupole scheme which cancels out many nonlinearities
Coupling-based round beam schemes are poorly compatible with off-axis injection
Acknowledgements:
Used contributions from R. Brinkmann, X. Nuel Gavalda, J, Keil, M. Tischer, R. Wanzenberg